## Slide 1: Small modular reactors
MTE4593 MATERIALS AND SUSTAINABILITY · ASSIGNMENT 2
Where they cut the most carbon, what holds them back, and the materials fix we propose
Leroy Jean · Sam · Victor Clarke
Notes: Leroy opens (about 15 seconds). “We’re looking at small modular reactors: where they would actually cut the most carbon, what stops them being built, and one materials change we think makes them better.” Then introduce the three speakers and their parts: Leroy on the problem and the technology, Sam on the life-cycle numbers, Victor on law, cost and public support.

## Slide 2: Coal is closing. What replaces its firm power?
640 g
NSW grid-average electricity factor, 2025–26 (operational)
5–6 g
Reference nuclear power, full life-cycle emissions (UNECE)
Retiring coal leaves a gap for reliable, low-carbon power. SMRs are pitched as one way to fill it.
Sources: DCCEEW (2025) National Greenhouse Accounts Factors; UNECE (2021) Life Cycle Assessment of Electricity Generation Options
Notes: Leroy (~1 min). The 640 g CO₂e/kWh figure is the published NSW grid-average, location-based electricity factor, and represents operational grid emissions. The 5–6 g is a UNECE estimate for conventional nuclear across its full lifecycle, not a measured BWRX-300 number. Therefore these figures are not identical system boundaries; they illustrate the broad contrast only. The next slides describe an actual project and then quantify a specific construction material change. Sources: DCCEEW National Greenhouse Accounts Factors 2025; UNECE Life Cycle Assessment of Electricity Generation Options (2021).

## Slide 3: The BWRX-300: a smaller, simpler boiling water reactor
300 MWe
About a fifth of a large reactor, built in a factory-style series
Passive cooling
Natural circulation and isolation condensers provide passive decay-heat removal after shutdown
>50% less concrete
Per MW, versus GE Hitachi’s large ESBWR design (vendor claim)
Source: GE Hitachi Nuclear Energy (2021) BWRX-300 presentation, Alberta Innovates SMR Learning Series
Notes: Leroy (about 1 minute). The BWRX-300 is GE Vernova Hitachi’s 300-megawatt boiling water reactor. Three points: it is small, about a fifth the size of a large reactor; it cools itself passively, with water circulating naturally and isolation condensers, so no pumps are needed to remove heat after shutdown; and GE Hitachi claims it uses less than half as much concrete and building volume per MW as its large ESBWR. Stress that this is the vendor’s claim, compared with their own large design, and it hasn’t been independently verified yet. Transition: “The first real test of those claims is being built right now in Canada.”

## Slide 4: Darlington, Ontario: the first SMR in the G7
Oct 2022
OPG applies for a licence to construct
Apr 2025
Canadian Nuclear Safety Commission grants the licence
May 2025
Ontario approves Unit 1; C$20.9 billion budget for all 4 units
2030
Unit 1 expected in service
C$20.9 billion is the full four-unit programme budget, including shared works (not only reactor hardware).
Sources: CNSC (2025); Government of Ontario (2025); OPG (2025)
Notes: Leroy (about 1 minute). Walk the timeline left to right. OPG applied for its construction licence in October 2022; the regulator granted it in April 2025; in May 2025 Ontario approved construction of Unit 1, within a C$20.9 billion budget for all four units (1,200 MW); Unit 1 is expected in service in October 2030, according to OPG’s Ontario Energy Board filing. Divide C$20.9 billion by 1,200 MW and you get about C$17 million per MW. That makes Darlington the first Western SMR with both a construction licence and a full budget, which is why our analysis uses it. Transition: “Here’s what we propose to do differently.”

## Slide 5: Pilot low-clinker LC³ concrete for future Darlington Units 2–4
OUR PROPOSAL
LOCATION
Darlington New Nuclear Project, Clarington, Ontario; Unit 1 already under construction
SCALE
Up to 3 × 300 MWe; ~50,000 m³ concrete/unit is a Polish BWRX-300 proxy
APPLICATION
First: eligible non-safety works. Later: steel-composite infill only if qualified
TECHNOLOGY
LC³ binder: calcined clay + limestone replace some Portland clinker
Reactor quantities and eligible share are provisional. Units 2–4 also require future licensing; Liddell is a separate Australian comparison.
Notes: Leroy (~1 minute 15 sec). Our materials-engineering proposal is to evaluate limestone calcined clay cement (LC³) for future BWRX-300 units at Darlington. The Canadian regulator currently licenses construction of Unit 1; Units 2–4 would require future licensing. Start with suitable non-safety-related site structures, then investigate use in structural or steel-composite reactor modules only after a dedicated qualification programme. This is NOT an approved material substitution. For screening, use the GE-Hitachi-supplied 2023 Polish BWRX-300 project estimate of 50,000 m³ of concrete for ONE plant—NOT a measured Darlington amount. The eligible percentage must be identified with OPG/design documentation; our example later assumes 40% only to illustrate method. Liddell in NSW remains a separate hypothetical deployment comparison, not the materials field trial. Primary data: BWRX-300 Ostrołęka (2023), Project Information Sheet, Table 14 p.83: https://am.lrv.lt/media/viesa/saugykla/2024/2/oHCKCUp7Lrs.pdf ; CNSC Darlington Project https://www.cnsc-ccsn.gc.ca/eng/reactors/new-reactor-power-plant-projects/new-reactor-power-plant-facilities/darlington-new-nuclear-project/

## Slide 6: Our assessment: full life-cycle boundary, materials quantified
Mining and milling
Conversion and enrichment
Fuel fabrication
Construction: concrete and steel
Operation
Decommissioning and waste
Functional unit
1 MWh of electricity delivered to the grid
Tools
Granta Eco Audit for construction materials; literature for fuel and waste
Our focus
Baseline vs LC³ concrete embodied CO₂ and energy
Reference inventory: BWRX-300 Ostrołęka Project Information Sheet (2023), Table 14; ISO 14040/44 framework
PRELIMINARY INVENTORY · ONE BWRX-300
50,000 m³ concrete
14,000 t steel
Polish project proxy, not confirmed Darlington quantities
Notes: Sam (~1 minute). The system boundary is cradle-to-grave and the functional unit is 1 MWh sent to the grid. But our OWN Granta Eco Audit is a screening assessment of the construction materials module, NOT a complete nuclear power plant LCA. Uranium mining, conversion, enrichment, fabrication, operation, spent fuel and decommissioning rely on peer-reviewed/agency literature and need explicit treatment in the report. A 2023 Polish BWRX-300 environmental project sheet reports 50,000 m³ concrete, 6,000 t steel elements and 8,000 t modular steel components per 300 MWe plant. These are project design estimates supplied by GE-Hitachi and are NOT Darlington as-built figures. Do not double count the reactor pressure vessel or piping unless the mass categories are confirmed. Our inventory is an illustrative bill of materials, and only an eligible share of concrete would be replaced. The use-phase claims and BWRX-300 lifetime carbon intensity cannot be validated by Granta alone. Cite: https://am.lrv.lt/media/viesa/saugykla/2024/2/oHCKCUp7Lrs.pdf (Table 14 PDF page 83), ISO 14040 and 14044.

## Slide 7
LC³ can reduce concrete production emissions
PUBLISHED M50 CONCRETE MIXES · CRADLE-TO-GATE CO₂-EQ PER m³
Peer-reviewed concrete mix comparison (Pillai et al., 2019)
Portland cement (OPC)
380 kg
LC³ (calcined clay + limestone)
270 kg
Both mixes were in the M50 strength class (28-day mean strengths: OPC 60.0 MPa; LC³ 56.7 MPa).
110 kg CO₂-eq saved/m³ · 28.9% reduction
CONDITIONAL SAVING PER BWRX-300 UNIT
2,200 t
CO₂-eq avoided IF 40% of 50,000 m³ qualifies for substitution
ΔCO₂ = 50,000 m³ × 40% × (380 − 270) kg/m³ ÷ 1,000 = 2,200 t
40% eligible is an ASSUMPTION; 50,000 m³ is a Polish BWRX-300 design proxy.
Sources: Pillai et al. (2019), Table 2, DOI:10.1016/j.cemconres.2018.11.019; BWRX-300 Ostrołęka (2023), Table 14.
Notes: Sam (~1.5 minutes). We have replaced the earlier hypothetical emission intensities with PUBLISHED NUMBERS from a peer-reviewed experimental/LCA study: Pillai et al. (2019), Cement and Concrete Research 118, 111–119, Table 2. M50-strength-category Portland concrete OPC-2 had a modelled cradle-to-gate carbon footprint of 380 kg CO2-eq per m3 and a mean 28-day cube strength of 60.0 MPa. M50-class limestone-calcined clay concrete LC3-2 had 270 kg CO2-eq/m3 and 56.7 MPa. Difference: 110 kg CO2-eq/m3, or 28.9%. These mixes were formulated and assessed for an Indian-context study; they are NOT an Ontario EPD nor certified for nuclear service. The source models material extraction, production, transport and ready-mix concrete manufacture through the plant gate; it does NOT measure a nuclear power plant lifecycle. A 2023 Polish BWRX-300 Project Information Sheet, Table 14, reports 50,000 m3 of concrete estimated for ONE 300 MWe unit. To illustrate Darlington, we assume only 40% of that total may be eligible for LC3 substitution, giving 20,000 m3 × 110 kg = 2,200 t CO2-eq per unit. The 40% eligibility share is NOT independently established: the true quantity could be smaller or zero until design/safety review. The result is not a measured Darlington saving, a whole-reactor life-cycle emission factor, nor our team's Granta result. For Darlington Units 2–4, the equivalent conditional scenario would be 3 × 2,200 = 6,600 t CO2-eq; do not claim as real savings. Materials selection would need actual strength/performance specs, tested concrete mix designs, Ontario EPDs, applicable nuclear standards and confirmation of how much concrete is eligible. Same technical input factors must be used on Slide 8 sensitivity examples. Primary paper full text: https://lc3.ch/wp-content/uploads/2022/03/Pillai-et-al.-2019-Service-life-and-life-cycle-assessment-of-reinforc.pdf ; DOI https://doi.org/10.1016/j.cemconres.2018.11.019 . Polish project https://am.lrv.lt/media/viesa/saugykla/2024/2/oHCKCUp7Lrs.pdf .

## Slide 8
What would make LC³ feasible in a nuclear project?
01 WORKABILITY
Flows through tight steel-composite spaces
Test slump flow, segregation, filling ability and early-age strength in full-scale mock-ups.
02 THERMAL & DURABILITY
Performs in large pours and harsh conditions
Test heat of hydration, shrinkage, cracking, permeability, freeze–thaw and long-term durability.
03 NUCLEAR QUALIFICATION
Meets required codes without delaying build
Confirm safety classification, material rules, QA/QC and regulator-approved design changes before use.
CO₂ sensitivity to eligible volume (Pillai: 110 kg CO₂-eq/m³ saving)
20% eligible → 1,100 t
40% eligible → 2,200 t
60% eligible → 3,300 t
Qualification: CSA N287.2; emissions intensity: Pillai et al. (2019), Table 2. Eligible share remains hypothetical.
Notes: Sam (~1 minute). The published M50 concrete carbon intensities are 380 kg CO2-eq/m3 for OPC and 270 for LC3 from Pillai et al. (2019) Table 2; difference 110 kg/m3. Under the SAME Polish 50,000 m3 BWRX-300 reference quantity, 20% concrete eligibility would mean 10,000 m3 replaced, saving 1,100 tonnes; 40% yields 20,000 m3 and 2,200 tonnes; 60% yields 30,000 m3 and 3,300 tonnes. None of the substitution fractions is verified for Darlington. The study's concrete mixes come from a non-Canadian context and do not prove compatibility with nuclear safety structures. Three technical tests: workability for steel-plate composites, heat/shrinkage/durability and project-specific nuclear qualification. Non-safety works first; safety-critical use conditional on design validation and regulator acceptance. CSA N287.2 is for materials in nuclear concrete containment structures; requirements for other structures depend on classification. Further research should obtain local EPDs, grade-specific specifications, admissible quantities, supplier logistics and curing/performance testing. Sources: Pillai et al 2019 DOI https://doi.org/10.1016/j.cemconres.2018.11.019; Polish project https://am.lrv.lt/media/viesa/saugykla/2024/2/oHCKCUp7Lrs.pdf .

## Slide 9: Illustrative grid averages: NSW offers greater CO₂ savings
One 300 MWe SMR at 90% capacity factor, compared with each grid’s CURRENT average intensity
NSW grid (640 g/kWh)
1.5 Mt
Ontario grid (35–74 g/kWh)
0.07–0.16 Mt
This is not a forecast: what the reactor actually displaces, commissioning date and future grid mix matter most.
Our calculation; grid factors: DCCEEW (2025), CER (n.d.), TAF (2025); nuclear 6 g/kWh: UNECE (2021). 90% capacity factor; average grid factors
Notes: Victor (~1 min). A transparent SCREENING EXAMPLE: at 300 MWe and 90% capacity factor, generation is 2.365 TWh/year. Avoided emissions if displacing each area's present-day AVERAGE intensity, using 6 g CO₂e/kWh illustrative nuclear LCA, are ~1.50 Mt CO₂e/year for NSW and 0.07–0.16 Mt for Ontario. This is not a validated forecast, and average grid carbon factors should not be mistaken for true hour-by-hour marginal generation avoided. Future grid decarbonisation and realistic project timelines could reverse or reduce this apparent gap. Darlington's value should be compared with actual marginal sources/dispatch, not simply average Ontario electricity. Source figures from presentation references; values should be confirmed against primary sources for the actual year.

## Slide 10: Nuclear power is banned in Australia today
BARRIER 1 · LAW
EPBC Act 1999, s140A
The Environment Minister must not approve a nuclear power plant
ARPANS Act 1998, s10
The national radiation regulator must not license one
NSW Act 1986, s8
Bans nuclear power reactors in NSW, including at Liddell
What would have to change: federal and NSW repeal, and a regulator able to license private operators. Canada’s construction licence alone took 29 months.
Sources: Environment Protection and Biodiversity Conservation Act 1999 (Cth); Australian Radiation Protection and Nuclear Safety Act 1998 (Cth); Uranium Mining and Nuclear Facilities (Prohibitions) Act 1986 (NSW); CNSC (2025)
Notes: Victor (about 1 minute). The first barrier is legal. Three laws stand in the way at Liddell. Section 140A of the federal EPBC Act stops the Environment Minister approving a nuclear power plant. Section 10 of the ARPANS Act stops ARPANSA, the national radiation regulator, from licensing one. And NSW’s own 1986 Act bans nuclear power reactors in the state (research reactors like Lucas Heights are exempt). The site owner, AGL, has also ruled out nuclear at Liddell. Even after repeal there’s a gap: ARPANSA only regulates Commonwealth entities, so a private operator would need a new licensing role. Politics: repeal needs a Senate majority, and both Labor and the Greens oppose it. A NSW repeal bill passed the upper house in May 2026 but has stalled in the lower house. In Canada, with an experienced regulator, OPG’s construction licence alone took 29 months. The non-technical solution is legislation plus a capable independent regulator, which needs political will that isn’t there yet. PROVISIONAL: confirm against the Acts and Hansard (02_Research/briefs/law-and-regulation.md). Transition: “Even if the law changed, there’s the cost.”

## Slide 11: SMRs are the most expensive new power in Australia
BARRIER 2 · COST
CSIRO GenCost 2025–26
Highest cost
of every option, even with Darlington’s real costs included. Firmed renewables are cheapest
NuScale, Idaho (US)
$58 → $89/MWh
Up 53% (2020 to 2022 dollars), even after about $30/MWh of subsidies. The 462 MW project was cancelled in 2023
What would have to change: government underwriting of first-of-a-kind risk, as Ontario and Canada are doing for Darlington.
Sources: CSIRO (2026) GenCost 2025–26; Power Engineering (2023); Canada Growth Fund and Building Ontario Fund (2025)
Notes: Victor (about 1 minute). Second barrier: cost. CSIRO’s GenCost reports (2024–25 and the current 2025–26 edition) rank SMRs as the most expensive new-build option in Australia. That holds even with real Darlington cost data, which landed inside CSIRO’s projected range. Renewables with firming and transmission are cheapest. The US warning is NuScale’s Carbon Free Power Project, planned at Idaho National Laboratory for a group of Utah utilities. Its target power price rose 53%, from $58 to $89 per MWh (2020 and 2022 dollars, so partly inflation), and the $89 already included about $30 per MWh of Inflation Reduction Act credits and Department of Energy support. Too few utilities signed up, and the 462 MW project was cancelled in November 2023. DOE had obligated about $232 million to it. Non-technical solution: someone has to carry the first-of-a-kind risk. In Canada the province and federal funds are taking equity stakes in Darlington. VICTOR TO CHECK: if asked for a number, the GenCost 2023–24 SMR range for 2030 was reported as $387–641/MWh; confirm in the report before quoting it. Transition: “Cost is one thing; does the public want it?”

## Slide 12: Most Australians back nuclear, but trust is fragile
BARRIER 3 · SOCIAL LICENCE
61%
support nuclear power for electricity; 37% oppose (Lowy Institute Poll 2024)
0.03
deaths per TWh from nuclear, against 24.6 for coal: the risk people fear is not the one that kills
What would have to change: host-community consent, a waste plan agreed up front, and local benefit sharing in the Hunter.
Sources: Lowy Institute (2024) Lowy Institute Poll; Our World in Data (2024) Death rates per unit of electricity production
Notes: Victor (about 1 minute). Third barrier: social licence. In the 2024 Lowy Institute Poll, 61% of Australians supported using nuclear power for electricity and 37% opposed it. So national support exists, but it is not consent from a host community. Perceived versus actual risk: per unit of electricity, nuclear has caused about 0.03 deaths per TWh, including Chernobyl and Fukushima, against about 24.6 for coal, mostly from air pollution (Our World in Data). People fear the accident, not the everyday pollution. Non-technical solutions: real consent from the Hunter community and First Nations, a waste plan agreed before construction, and local benefit sharing. VICTOR TO CHECK: confirm the coal figure (24.6) on the Our World in Data chart before presenting. Transition: “Last barrier: where the fuel comes from.”

## Slide 13: Australia has the uranium, but someone else enriches it
BARRIER 4 · FUEL SUPPLY
28%
of the world’s identified recoverable uranium is in Australia, the largest share
43%
of global enrichment capacity is Russian (2025). Australia has none of its own
Enrichment HHI ≈ 3,000, highly concentrated (above 1,800). Mitigation: long-term contracts with allied enrichers.
Sources: OECD NEA and IAEA (2025) Uranium 2024: Resources, Production and Demand; World Nuclear Association (2025)
Notes: Victor (about 1 minute). Fourth barrier: fuel supply. Australia holds about 28% of the world’s identified recoverable uranium, the largest share of any country (NEA/IAEA Red Book 2024). But we mine it and ship it as ore concentrate: there is no conversion or enrichment here. Russia holds about 43% of global enrichment capacity (42.8% in 2025, World Nuclear Association). The Herfindahl-Hirschman index (HHI) adds up the squared market shares; the US DOJ/FTC 2023 Merger Guidelines treat anything above 1,800 as highly concentrated. Enrichment comes out at about 3,000, 3,600 without Russia, and about 5,600 once China is also excluded, when it is essentially just Urenco and Orano. Uranium mining (2,341) and conversion (2,111) are also highly concentrated. That is a geopolitical risk for any reactor here. Mitigation (it reduces a buyer’s exposure, not the HHI): long-term contracts with allied enrichers such as Urenco and Orano, and over time, possibly domestic conversion. PROVISIONAL: these figures come from search extracts of the WNA pages, not the pages themselves (network blocked). Confirm them before submitting. Working: 03_LCA_Calculations/results/hhi.md. Transition: “So, is it worth it?”

## Slide 14: Low-carbon electricity, but deployment and materials matter
VERDICT · TRIPLE BOTTOM LINE
Pillar | Rating | Why
Environmental | Mixed | Nuclear is low-carbon; LC³ may lower construction CO₂ in approved applications.
Economic | Weak | High capital and delivery risk; LC³ must not raise cost or slow construction.
Social | Mixed | Safety, nuclear waste, local consent and skilled supply chains need attention.
Darlington: trial LC³ in suitable works and qualify it before safety-critical use. Liddell: cost, law and realistic timing dominate the Australian case.
Notes: Victor (~1 minute) and close. Separate TWO questions. 1) Darlington materials proposal: could a qualification programme for LC³ lower construction emissions without compromising structural integrity or slowing the first commercial demonstration? Use suitable non-safety works first and collect real material-specific EPD data, tests and construction quantities. On present screening assumptions, the saving is about 2,200 t CO₂e per unit and is not yet a verified Granta number. 2) The Australian nuclear question: SMRs can generate low-lifecycle-carbon electricity, but have high project cost, licensing barriers, grid-displacement uncertainties and long lead times. Our conclusion is conditional, not an anti-nuclear claim: better concrete helps but does not solve financing, licensing or timing. Remove any energy-per-dollar multiplier until sensitivity calculations and system boundaries are confirmed. Mention that we would update the triple-bottom-line assessment after the life-cycle results and stakeholder analysis are complete.

## Slide 15: References
CSIRO, 2026. GenCost 2025–26 Final Report. Canberra: CSIRO.
DCCEEW, 2025. Australian National Greenhouse Accounts Factors 2025. Canberra: Commonwealth of Australia.
GE Hitachi Nuclear Energy, 2021. BWRX-300 Small Modular Reactor. Alberta Innovates SMR Learning Series.
Krall, L.M., Macfarlane, A.M. and Ewing, R.C., 2022. Nuclear waste from small modular reactors. PNAS, 119(23), e2111833119.
Lowy Institute, 2024. Lowy Institute Poll 2024. Sydney: Lowy Institute.
NucNet, 2025. Canada’s regulator issues construction licence for Darlington small modular reactor.
OECD NEA and IAEA, 2025. Uranium 2024: Resources, Production and Demand. Paris: OECD Publishing.
Ontario Government, 2024. Ontario energy snapshot. Toronto: Government of Ontario.
Our World in Data, 2024. Death rates per unit of electricity production.
Scrivener, K., Martirena, F., Bishnoi, S. and Maity, S., 2018. Calcined clay limestone cements (LC3). Cement and Concrete Research, 114, pp.49–56.
Power Engineering, 2023. Facing mounting costs, NuScale cancels small modular reactor project in Utah.
UNECE, 2021. Life Cycle Assessment of Electricity Generation Options. Geneva: United Nations.
World Nuclear Association, 2025. Uranium Enrichment; Conversion and Deconversion. London: WNA.
World Nuclear News, 2022. OPG applies for construction licence for Darlington SMR.
World Nuclear News, 2025. OPG secures government equity financing for SMR project.
Environment Protection and Biodiversity Conservation Act 1999 (Cth) s140A; Australian Radiation Protection and Nuclear Safety Act 1998 (Cth) s10.
BWRX-300 Ostrołęka sp. z o.o., 2023. Small Modular Nuclear Power Plant: Project Information Sheet, Table 14, p. 83.
CSA Group, 2026. CSA N287.2-2026: Material requirements for concrete containment structures for nuclear power plants.
Canadian Nuclear Safety Commission, 2026. Darlington New Nuclear Project: licences and regulatory hold points.
Pillai, R.G. et al. 2019, ‘Service life and life cycle assessment of reinforced concrete systems with limestone calcined clay cement (LC³)’, Cement and Concrete Research, vol. 118, pp. 111–119. doi:10.1016/j.cemconres.2018.11.019.
Notes: Selected full URLs for the revised technical analysis:
BWRX-300 Ostrołęka sp. z o.o. (2023) Project Information Sheet, Table 14, PDF p.83: https://am.lrv.lt/media/viesa/saugykla/2024/2/oHCKCUp7Lrs.pdf
Scrivener, K. et al. (2018) Calcined clay limestone cements (LC3), Cement and Concrete Research 114:49–56: https://doi.org/10.1016/j.cemconres.2017.08.017
CSA Group (2026), CSA N287.2-2026: https://webstore.ansi.org/standards/csa/csan2872026
Canadian Nuclear Safety Commission (2026), Darlington New Nuclear Project: https://www.cnsc-ccsn.gc.ca/eng/reactors/new-reactor-power-plant-projects/new-reactor-power-plant-facilities/darlington-new-nuclear-project/
The original references on this slide are retained from the team's submitted draft. For the final version, cross-check every numerical claim against the referenced document and include full URLs/access dates required by the course.
Added citation used on Slides 7–8: Pillai, R.G. et al. (2019), Cement and Concrete Research, vol. 118, pp. 111–119, Table 2: https://doi.org/10.1016/j.cemconres.2018.11.019 ; accessible paper: https://lc3.ch/wp-content/uploads/2022/03/Pillai-et-al.-2019-Service-life-and-life-cycle-assessment-of-reinforc.pdf